## Slide 1
Space Communication
This Chapter includes:
Space Communication
Power Density, Attenuation
Range of Electromagnetic Waves
Ground Wave Propagation
Sky Wave Propagation
Space Wave Propagation
TV Transmission and Height of TV Antenna
Satellite Communication
Remote Sensing Satellites
Dr. Anjana Kumari.

## Slide 2
Space Communication:
Space Communication means free space communication.
A free space does not have solid particles or ionised particles and it has no gravitational or other fields of its own. When the frequency of transmitted wave is very high the actual space is considered nearly a free space.
Power Density:
Power density is radiated power per unit area and is inversely proportional to the square of distance from the source.
Antenna:
Antenna is a device which acts as an emitter of electromagnetic waves and it also acts as a first receiver of energy.
Attenuation:
Attenuation is the loss of power of radiation due to absorption of energy in space and power density goes on decreasing as the electromagnetic waves go away from their source.
It is proportional to the square of the distance travelled and is generally measured in decibel (dB).

## Slide 3
S. No. | Name of the frequency range (Band) | Short Form | Frequency Range
1 | Very Low Frequency | VLF | 3 kHz to 30 kHz
2 | Low Frequency | LF | 30 kHz to 300 kHz
3 | Medium Frequency or Medium Wave | MF or MW | 300 kHz to 3 MHz
4 | High Frequency or Short Wave | HF or SW | 3 MHz to 30 MHz
5 | Very High Frequency | VHF | 30 MHz to 300 MHz
6 | Ultra High Frequency | UHF | 300 MHz to 3,000 MHz
7 | Super High Frequency or Micro Waves | SHF | 3,000 MHz to 30,000 MHz (3 GHz to 30 GHz)
8 | Extremely High Frequency | EHF | 30 GHz to 300 GHz
Range of Electromagnetic Waves:

## Slide 4
Depending on the frequency, radio waves and micro waves travel in space in different ways depending on the behaviour of these waves w.r.t. the earth and the atmosphere. They are:
Ground wave propagation
Sky (or ionospheric) wave propagation
Space (or tropospheric) wave propagation
Ground wave propagation: (AM Radio waves)
In ground wave propagation, the radio waves (AM) travel along the surface of the earth. These waves are called ground waves or surface waves.
In fact, these waves are not confined to surface of the earth but are guided along the earth’s surface and they follow the curvature of the earth.
The energy of the radio waves decreases as they travel over the surface of the earth due to the conductivity and permittivity of the earth’s surface.
Attenuation increases with the increase in frequency.
Therefore, the ground waves are limited to frequency of 1.5 MHz (1500 kHZ) or wavelength of 200 m.
Propagation of Electromagnetic Waves:

## Slide 5
Earth
Ground waves progress along the surface of the earth and must be vertically polarised to prevent from short-circuiting the electric component.
A wave induces currents in the earth over which it passes and thus loses some energy by absorption. This is made up by energy diffracted downward from the upper portions of the wavefront.
Another way of attenuation is due to diffraction and gradual tilting of the wavefront.
The increasing tilt of the wavefront causes greater short-circuiting of electric field components of the wave.
Eventually, at some distance from the antenna, the wave “lies down and dies”.
The maximum range of a transmitter depends on its frequency as well as its power.
In MF band, the range can not be increased only by increasing its power because propagation is definitely limited by its tilt.
Direction of propagation of wave
T
Successive Wavefronts
θ
θ – Angle of diffraction
N

## Slide 6
Height of Communication Satellite:
The area of the earth from which a satellite is visible increases with the altitude.
At altitudes below 10,000 km, the number of satellites required for global coverage would be excessive.
At altitudes above 20,000 km, the time taken by signals may be large enough to cause confusion in telephonic conversation.
If time-delay difficulties are ignored, then a synchronous satellite at 36,000 km height can be advantageously used.
Earth-Track Integral System for Communication Satellites:
If several satellites are spaced around the same orbit in space, the tracks of the satellites will be different due to Earth’s rotation about its own axis.
If four satellites are placed into different orbits with their ascending modes displaced successively by 30° intervals to the east direction, the difference, in effects of Earth’s rotation, can be counteracted and the paths of all the satellites relative to the Earth will be the same.
Such Earth-Track integral systems can be arranged to have the satellite period an integral factor of the sidereal day in order to have the same track repeated day after day.

## Slide 7
Remote Sensing Satellites:
‘Remote Sensing’ is obtaining information about an object by observing it from a distance and without coming into actual contact with it.
The orbit of a remote sensing satellite is such that the satellite passes over a particular latitude at approximately the same local time. i.e. the position of the Sun with respect to a point on the Earth remains approximately the same as the satellite passes over it. Such orbits are called Sun-synchronous orbits.
A remote sensing satellite takes photographs of a particular region with nearly the same illumination every time it passes through that region.
Applications:
In Geology
In Agriculture
In Forestry
In Land Mapping
In Ocean and Coastal Data
In Monitoring Environmental Conditions
In Biodiversity
In Ground Water Management
In Flood Damage Assessment
In the Field of Defence
In Mapping Wastelands
In Early Warning Systems (Natural Calamities)
In Management of Water Resources
In Fisheries Sectors
In Tourism Industry
In Planning Pipeline Routs, Ring Roads and Urban Settlements